## Slide 1: CS-234: Computer Organization and Assembly Language Cache
Dr. Sara Shakil Qureshi

## Slide 2: Computer Organization

## Slide 3: Interfacing in Microprocessor
The process of connecting external devices such as memory and I/O peripherals to the microprocessor, allowing control and data exchange.
Types
Memory Interfacing
I/O Interfacing
  Memory-Mapped I/O and Isolated I/O
Data transfer
Timing and control
Address decoding

## Slide 4: IA-32 Modes of Operation
Real Mode
Protected Mode
System Management Mode
Virtual 8086 Mode

## Slide 5: IA-32 Modes of Operation
Real Mode
Can access only 1MB Memory (beyond 80286) – 16-bit
For MS-DOS
One task at a time (Single-Tasking), no protection
Programs can access Shared Memory Locations
Protected Mode
Can access only 4GB RAM, 32-bit
For Windows, Linux
Allows multi-tasking, memory protection
Memory Reservation for each Program

## Slide 6: IA-32 Modes of Operation
System Management Mode (SMM)
Special purpose mode used by system/firmware.
Implementing Functions : Power Management, hardware control & System Security
Usually implemented by Computer Manufacturers
Invisible to OS
Virtual Mode
Being in Protected Mode: The processor can directly execute a program in Real Mode
Can access only 1MB Virtual Memory (beyond 80286) – Emulating real mode inside protected mode

## Slide 7: IA-32 Memory Management
Segmented Memory Model – Real Mode
– Calculating linear addresses
Flat Memory Model – Protected Mode

## Slide 8: Segmented Memory Model
Format ~ Segment : Offset

## Slide 9: Segmented Memory Model
Linear Address Calculations:
1000h:5000h Calculate linear address.
Linear Address Calculations:
New Seg. Address 10000h
Add offset into new Address Offset Address 5000h
Linear Address =15000h

## Slide 10: Segmented Memory Model

## Slide 11: Memory
Volatile memory (RAM)
Information decays naturally or is lost when electrical power is switched off
Nonvolatile memory (ROM)
Once recorded, information remains without deterioration until deliberately changed
No electrical power is needed to retain information
Magnetic-surface memory (HDDs, magnetic tapes)
Are non-volatile

## Slide 12: Memory
Semiconductor memory
May be either volatile or nonvolatile
Nonerasable memory
Cannot be altered, except by destroying the storage unit
Semiconductor memory of this type is known as read-only memory (ROM)
For RAM the organization is a key design issue

## Slide 13: Memory
Types of RAM
SRAM:
Memory cell uses Flip-Flop to store a Bit
Requires 6 Transistors
Holds Data as long as power supplied
Faster and reliable but more costly
DRAM:
Memory cell uses MOS transistor and capacitor to store a bit
More compact than SRAM
Stores data in capacitors
Typical refresh rate 15.625 µs

## Slide 14: Memory Hierarchy
In computer architecture, it is the organization of different types of memory, such as registers, cache and main memory based on speed, capacity and cost.
Faster, smaller and more expensive memory closer to the CPU
Slower, larger and cheaper memory far from the CPU

## Slide 15: Memory Hierarchy
Design constraints on a computer’s memory conclude by three questions:
How much, how fast, how expensive
There is a trade-off among access time, cost, and capacity
Faster access time, greater cost per bit
Greater capacity, smaller cost per bit
Greater capacity, slower access time

## Slide 16: Memory Hierarchy

## Slide 17: Cache
It is a small high speed memory that acts as a buffer between the CPU and main memory
Stores frequently accessed data and instructions
Advantages:
  Faster data access
  Improved system performance
  Reduced latency

## Slide 18: Cache
Cache Hit
It occurs when the requested data is found in the cache, providing quick data retrieval.
Cache Miss
It happens when the requested data is not found in the cache and requires to be retrieved from the main memory.
High cache miss rates slow down the performance

## Slide 19: Cache Operation
CPU requests contents of memory location.
Check cache for this data.
If present, get from cache (fast).
If not present, read required block from main memory to cache.
Then deliver from cache to CPU.

## Slide 20: Cache Operation Flowchart

## Slide 21: Cache Sizes

## Slide 22: Memory

## Slide 23: Cache and Main Memory
Computer Organization and Architecture, Eleventh Edition by William Stallings

## Slide 24: Cache and Main Memory
Computer Organization and Architecture, Eleventh Edition by William Stallings

## Slide 25
Block: The minimum unit of transfer between cache and main memory.
Frame: To distinguish between the data transferred and the chunk of physical memory
Line: A portion of cache memory capable of holding one block, (i.e., all bytes of the line are typically drawn in one row).
Tag: A portion of a cache line that is used for addressing purposes

## Slide 26: Memory Mapping
Because there are fewer cache lines than main memory blocks, an algorithm is needed for mapping main memory blocks into cache lines
Direct Mapping
Associative Mapping
Set Associative Mapping
Computer Organization and Architecture, Eleventh Edition by William Stallings

## Slide 27: Direct
Each block of main memory can map to only one unique line of cache.

## Slide 28: Associative
Each block of main memory can map to any line of cache.
Tag portion of address used to check every line for hit on that line.

## Slide 29: Set Associative
Each block of main memory maps to one unique cache set.
Line portion of address used to access cache set
Tag portion used to check every line in that set for hit on that line.
Computer Organization and Architecture, Eleventh Edition by William Stallings

## Slide 30: Direct Mapping
Computer Organization and Architecture, Eleventh Edition by William Stallings

## Slide 31: Example
Main Memory Size = 32B
Cache Size = 16B
Block Size = 4 Bytes
How many lines for Cache memory? 16 B /4 B=4 lines
How many address lines for accessing cache memory lines?
2^2 =4, address lines for Cache is 2
How many Blocks in main memory?
32 B/4 B =8 blocks
How many address lines for accessing Main memory?
2^5 =32 , address lines for main memory is 5
Computer Organization and Architecture, Eleventh Edition by William Stallings

## Slide 32: Example
Main Memory Size = 16 MB
Cache Size = 64 KB
Block Size = 4 Bytes
How many lines for Cache memory? 64 KB /4 B=16 K lines
How many address lines for accessing cache memory lines? 2^14 =16 K, address lines for Cache is 14
How many Blocks in main memory?
16 MB/4 B =4 Mega blocks
How many address lines for accessing Main memory?
2^24 =16 M, address lines for main memory is 24
Address length =24= (22+2)=(s + w) bits
Address length =24= (tag+line+word)= (8+14+2)
Computer Organization and Architecture, Eleventh Edition by William Stallings

## Slide 33: Direct Mapping
When the cache hardware is presented with an address from the processor, the Line Number portion of the address is used to index into the cache. A compare function compares the tag of that line with the Tag field of the address.
  If there is a match (hit), an enable signal is sent to a select function, which uses the Offset field of the address and the Line Number field of the address to read the desired word or byte from the cache.
  If there is no match (miss) then the select function is not enabled and data is accessed from main memory, or the next level of cache.

## Slide 34: Direct Mapping
Address length = (s + w) bits
Number of addressable units = 2^(s+w) words or bytes
Block size = line size = 2^w words or bytes
Number of blocks in main memory = 2^(s+ w)/2^w = 2s
Number of lines in cache = m = 2^r
Size of tag = (s – r) bits
Computer Organization and Architecture, Eleventh Edition by William Stallings